| Pg.1 |
| --- |
| DATA – METRICS |
| CONVERSION TABLE – U.S. TO METRIC |
| LENGTH | FROM U.S. | TO METRIC | MULTIPLY BY |
|  | Inches | Millimeters | 25.40 |
|  | Inches | Centimeters | 2.54 |
|  | Inches | Meter | 0.0254 |
|  | Feet | Millimeters | 304.8 |
|  | Feet | Centimeters | 30.48 |
|  | Feet | Meters | 0.3048 |
|  | Yard | Centimeters | 91.44 |
|  | Yard | Meter | 0.9144 |
| WEIGHT | Lb. | Kilogram | 0.4536 |
|  | Oz./ft.² | G/M² | 305.16 |
|  | Lb./ft. | KG/M | 1.488 |
| AREA | Sq. Mile | KM² | 2.59 |
|  | Sq. Ft. | M² | 0.0929 |
|  | Sq. Inch | MM² | 645.16 |
|  | Acre | M² | 4046.87 |

| Pg.2 |
| --- |
| METRICS |
| CHAIN LINK WIRE SIZE – METRIC EQUIVALENT NOTE: Conversion numbers are approximate. |
| GAUGE | DECIMAL INCHES | (MM) MILLIMETERS |
| 6 | 0.192 | 4.88 |
| 9 | 0.148 | 3.76 |
| 11 | 0.120 | 3.05 |
| 11 1/2 | 0.113 | 2.87 |
| CHAIN LINK HEIGHT – METRIC EQUIVALENT NOTE: Conversion numbers are approximate. |
| TRADE SIZE | INCHES | (MM) MILLIMETERS |
| 3’ | 36” | 914 |
| 3 ½’ | 42” | 1067 |
| 4’ | 48” | 1219 |
| 5’ | 60” | 1524 |
| 6’ | 72” | 1829 |
| 7’ | 84” | 2134 |
| 8’ | 96” | 2438 |
| 9’ | 108” | 2743 |
| 10’ | 120” | 3048 |
| 12’ | 144” | 3658 |
| CHAIN LINK MESH SIZE – METRIC EQUIVALENT NOTE: Conversion numbers are approximate. |
| TRADE SIZE | DECIMAL INCHES | (MM) MILLIMETERS |
| 3/8” | 0.375 | 9.52 |
| ½” | 0.500 | 12.70 |
| 5/8” | 0.625 | 15.87 |
| ¾” | 0.750 | 19.05 |
| 1” | 1.000 | 25.40 |
| 1 ¼” | 1.250 | 31.75 |
| 1 ½” | 1.500 | 38.10 |
| 1 ¾” | 1.750 | 44.45 |
| 2” | 2.000 | 50.80 |
| 2 1/8” | 2.125 | 53.98 |
| 2 ¼” | 2.250 | 57.15 |

| Pg.3 |
| --- |
| METRICS |
| FULL WEIGHT PIPE (SCHEDULE 40) = METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| TRADE SIZE | OUTSIDE DIAMETER | WALL THICKNESS | WEIGHT |
|  | Decimal Inches | (MM) Millimeters | Decimal Inches | (MM) Millimeters | Lbs./Ft. | KG/M |
| 1 3/8” | 1.315 | 33.40 | 0.133 | 3.38 | 1.68 | 2.50 |
| 1 5/8” | 1.660 | 42.20 | 0.140 | 3.56 | 2.27 | 3.40 |
| 1 7/8” | 1.900 | 48.30 | 0.145 | 3.68 | 2.72 | 4.00 |
| 2 3/8” | 2.375 | 60.30 | 0.154 | 3.91 | 3.65 | 5.40 |
| 2 7/8” | 2.875 | 73.00 | 0.203 | 5.16 | 5.79 | 8.60 |
| 3 ½” | 3.500 | 88.90 | 0.216 | 5.49 | 7.58 | 11.30 |
| 4” | 4.000 | 101.60 | 0.226 | 5.74 | 9.11 | 13.60 |
| 4 ½” | 4.500 | 114.30 | 0.237 | 6.02 | 10.79 | 16.10 |
| 6 5/8” | 6.625 | 168.30 | 0.280 | 7.11 | 18.97 | 28.30 |
| 8 5/8” | 8.625 | 219.10 | 0.322 | 8.18 | 28.55 | 42.50 |
| FULL WEIGHT PIPE (SCHEDULE 40) = METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| TRADE SIZE | OUTSIDE DIAMETER | WALL THICKNESS | WEIGHT |
|  | Decimal Inches | (MM) Millimeters | Decimal Inches | (MM) Millimeters | Decimal Inches | (MM) Millimeters |
| 1 3/8” | 1.315 | 33.40 | 0.104 | 2.64 | 1.34 | 2.00 |
| 1 5/8” | 1.660 | 42.20 | 0.111 | 2.81 | 1.83 | 2.80 |
| 1 7/8” | 1.900 | 48.30 | 0.120 | 3.05 | 2.28 | 3.40 |
| 2 3/8” | 2.375 | 60.30 | 0.130 | 3.30 | 3.12 | 4.70 |
| 2 7/8” | 2.875 | 73.00 | 0.160 | 4.06 | 4.64 | 6.90 |
| 3 ½” | 3.500 | 88.90 | 0.160 | 4.06 | 5.71 | 8.50 |
| 4” | 4.000 | 101.60 | 0.160 | 4.06 | 6.56 | 9.80 |
| POST LENGTH – METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| TRADE SIZE | (MM) Millimeters | TRADE SIZE | (MM) Millimeters |
| 6’ | 1829 | 10’ | 3048 |
| 6’ 6” | 1981 | 10’ 6” | 3200 |
| 7’ | 2134 | 11’ | 3353 |
| 7’ 6” | 2286 | 11’ 6” | 3505 |
| 8’ | 2438 | 12’ | 3658 |
| 8’ 6” | 2591 | 12’ 6” | 3810 |
| 8’ 8” | 2641 | 13’ | 3962 |
| 9’ | 2743 | 13’ 6” | 4115 |
| 9’ 6” | 2896 | 14’ | 4267 |

| Pg.4 |
| --- |
| METRICS |
| WIRE GAUGE – METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| GAUGE NO | DECIMAL INCHES | (MM) MILLIMETERS | GAUGE NO | DECIMAL INCHES | (MM) MILLIMETERS |
| 5 | 0.2070 | 5.25 | 13 | 0.0915 | 2.32 |
| 6 | 0.1920 | 4.88 | 14 | 0.0800 | 2.03 |
| 7 | 0.1770 | 4.50 | 15 | 0.0720 | 1.83 |
| 8 | 0.1620 | 4.11 | 16 | 0.0625 | 1.59 |
| 9 | 0.1483 | 3.76 | 17 | 0.0540 | 1.37 |
| 10 | 0.1350 | 3.43 | 18 | 0.0475 | 1.21 |
| 11 | 0.1205 | 3.05 | 19 | 0.0410 | 1.04 |
| 12 | 0.1055 | 2.68 | 20 | 0.0348 | 0.88 |
| SHEET GAUGE (H.R.P. & O.) – METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| GAUGE NO | DECIMAL INCHES | (MM) MILLIMETERS | GAUGE NO. | DECIMAL INCHES | (MM) MILLIMETERS |
| 5 | 0.2092 | 5.31 | 13 | 0.0897 | 2.28 |
| 6 | 0.1943 | 4.94 | 14 | 0.0747 | 1.90 |
| 7 | 0.1793 | 4.55 | 15 | 0.0673 | 1.71 |
| 8 | 0.1644 | 4.18 | 16 | 0.0598 | 1.52 |
| 9 | 0.1495 | 3.80 | 17 | 0.0538 | 1.37 |
| 10 | 0.1345 | 3.42 | 18 | 0.0478 | 1.21 |
| 11 | 0.1196 | 3.04 | 19 | 0.0418 | 1.06 |
| 12 | 0.1046 | 2.66 | 20 | 0.0359 | 0.91 |

| Pg.5 |
| --- |
| METRICS |
| COMMON DIMENSIONS – METRIC EQUIVALENTS NOTE: Conversion numbers are approximate. |
| TRADE SIZE | DECIMAL INCHES | (MM) MILLIMETERS | TRADE SIZE | DECIMAL INCHES | (MM) MILLIMETERS |
| 3/8” | 0.375 | 9.50 | 2 3/8” | 2.375 | 60.30 |
| ½” | 0.500 | 12.70 | 2 7/8” | 2.875 | 73.00 |
| 5/8” | 0.625 | 15.90 | 3 ½” | 3.500 | 88.90 |
| 1” | 1.000 | 25.40 | 4” | 4.000 | 101.60 |
| 1 3/8” | 1.315 | 33.40 | 4 ½” | 4.500 | 114.30 |
| 1 5/8” | 1.660 | 42.20 | 6 5/8” | 6.625 | 168.30 |
| 1 7/8” | 1.900 | 48.30 | 8 5/8” | 8.625 | 219.10 |

| Pg.6 |
| --- |
| CONCRETE ESTIMATING |
| HOLES PER CUBIC YARD OF CONCRETE NOTE: Conversion numbers are approximate. |
| DEPTH | DIAMETER OF HOLE |
|  | 6” | 8” | 10” | 12” | 16” | 18” | 24” |
| 24” | 68.8 | 38.5 | 24.3 | 17.0 | 9.5 | 7.6 | 4.0 |
| 30” | 55.0 | 31.0 | 19.7 | 13.7 | 7.7 | 6.0 | 3.0 |
| 36” | 45.5 | 25.8 | 16.5 | 11.1 | 6.0 | 5.1 | 2.7 |
| 42” | 39.3 | 22.1 | 14.1 | 9.8 | 5.5 | 4.0 | 2.5 |
| 48” | 34.4 | 19.0 | 12.0 | 8.6 | 4.8 | 3.8 | 2.0 |
| 54” | 30.6 | 17.0 | 10.7 | 7.6 | 4.3 | 3.3 | 1.7 |
| CUBIC YARDS OF CONCRETE PER HOLE NOTE: Conversion numbers are approximate. |
| DEPTH | DIAMETER OF HOLE |
|  | 6” | 8” | 10” | 12” | 16” | 18” | 24” |
| 24” | .0145 | .0260 | .0412 | .0581 | .1030 | .1316 | .2338 |
| 30” | .0182 | .0323 | .0508 | .0730 | .1299 | .1667 | .2923 |
| 36” | .0220 | .0388 | .0606 | .0870 | .1538 | .1961 | .3507 |
| 42” | .0254 | .0455 | .0709 | .1020 | .1818 | .2273 | .4091 |
| 48” | .0291 | .0515 | .0806 | .1163 | .2083 | .2632 | .4675 |
| 54” | .0327 | .0581 | .0916 | .1316 | .2326 | .2941 | .5259 |

| Pg.7 |
| --- |
| DATA POST SPACING |
| LINE POST SPACING CHART |
| SPACE |  | SET POST ON CENTER | SPACE |  | SET POST ON CENTER |
| 30’………………………….…...…………10’ | 80’………………………………………….10’ |
| 31’….………………………….…………7’9” | 81’…………………………………………...9’ |
| 32’….…………………..……….…..…...…8’ | 82’……………………..………………...9’1” |
| 33’….……………………….……………8’3” | 83’………………………..……………...9’3” |
| 34’…….…….……………………………8’6” | 84’………………………..……………...9’4” |
| 35’…….………..………………….…….8’9” | 85’…………………………..…………...9’6” |
| 36’…….………....……..………………….9’ | 86’………………………..……………...9’7” |
| 37’…….………………………………….9’3” | 87’……………………..………………...9’8” |
| 38’…….………...……………………….9’6” | 88’…………………………..…………...9’9” |
| 39’…….………..…..………..………….9’9” | 89’……………………………………...9’10” |
| 40’……….…………….....….……………10’ | 90’……………………………..…………….9’ |
| 41’……….……….………..….…………8’2” | 91’………………………..……………...9’2” |
| 42’……….………………….……………8’5” | 92’……………………..………………...9’2” |
| 43’……….………………….……………8’6” | 93’…………………..…………………...9’3” |
| 44’……….………………….……………8’9” | 94’…………………………..…………...9’5” |
| 45’……….…………………….…………….9’ | 95’………………………..……………...9’6” |
| 46’……….……………………………….9’2” | 96’………………………………..……...9’7” |
| 47’……….……………………………….9’5” | 97’………………………………..……...9’7” |
| 48’……….……………………………….9’7” | 98’……………………………..………...9’8” |
| 49’……….……………………………….9’9” | 99’…………………………..…………...9’9” |
| 50’……….…………………………………10’ | 100’………………………..…..………….10’ |
| 51’……….……………..……………..…8’6” | 101’……………………………………...9’2” |
| 52’……….……………….………………8’8” | 102’……………………………………...9’3” |
| 53’……….………………..……………8’10” | 103’……………………………………...9’4” |
| 54’……….……………………..……………9’ | 104’……………………………………...9’5” |
| 55’……….……………………….………9’2” | 105’……………………………………...9’6” |
| 56’……….……………….………………9’4” | 106’……………………………………...9’7” |
| 57’……….………………….……………9’6” | 107’……………………………………...9’8” |
| 58’………….………...………..…………9’8” | 108’……………………………………...9’9” |
| 59’…………….………...………………9’10” | 109’………………………….………...9’10” |
| 60’…………….……….…..………………10’ | 110’…………………………….………….10’ |
| 61’…………….………..…………………8’8” | 111’……………………………………...9’3” |
| 62’…………….………..………….……8’10” | 112’………………………...…………...9’4” |
| 63’…………….……….……..……….…….9’ | 113’……………………………………...9’5” |
| 64’…………….……….…………………….9’ | 114’……………………………………...9’6” |
| 65’…………….……..…..……………….9’3” | 115’……………………………………...9’7” |
| 66’…………….……..……..…………….9’5” | 116’………………………...…………...9’8” |
| 67’…………….…………….…………….9’7” | 117’……………………………………...9’9” |
| 68’…………….……………….………….9’8” | 118’……………………….…………...9’10” |
| 69’…………….………………..……….9’10” | 119’……………………….…………...9’10” |
| 70’……………….……..…….…………….10’ | 120’……………………….……………….10’ |
| 71’……………….……..……..………….8’9” | 121’……………………………………...9’3” |
| 72’……………….……..…….…..………….9’ | 122’……………………………………...9’4” |
| 73’……………………………..………….9’2” | 123’……………………..…….………...9’5” |
| 74’……………….…….………………….9’3” | 124’……………………………………...9’6” |
| 75’……………….……….……………….9’4” | 125’…………………………...………...9’7” |
| 76’……………….………....…………….9’5” | 126’……………………………………...9’8” |
| 77’……………….…………....………….9’7” | 127’……………………………………...9’9” |
| 78’……………………………..………….9’9” | 128’………………………….………...9’10” |
| 79’………………………………..…….9’ 10” | 129’………………………….………...9’10” |

| Pg.8 |
| --- |
| DATA – SPECIFICATIONS |
| AMERICAN SOCIETY FOR TESTING AND MATERIALS (ASTM) |
| DESIGNATION | PRODUCT REQUIRED | PAGE NO. |
| ASTM F 1083 | Domestic Full Weight Pipe | J-20, 21 |
| ASTM F 669 | DQ40 Pips | J-15, 16 |
| ASTM A392 |  |  |
| CLASS 1 | Chain Link Fabric 1.2oz./ft.² Zinc Coating | M-2 thru 5 |
| CLASS 2 | Chain Link Fabric 2.0oz./ft.² Zinc Coating | M-4 |
| ASTM A 491 | Aluminized Chain Link Fabric | M-6 |
| ASTM F 668 |  |  |
| CLASS 2a | Master Bond™ Chain Link Fabric | M-11 |
| CLASS 2b | Fusion Bonded Chain Link Fabric | S-33 |
| ASTM A 824 |  |  |
| TYPE l | Coil String Tension Wire .40 oz/ft.² Aluminum Coating | C-6 |
| TYPE II |  |  |
| CLASS 1 | Coil Spring Tension Wire .80 oz/ft.² Zinc Coating | C-6 |
| CLASS 2 | Coil Spring Tension Wire 1.2 oz/ft.² Zinc Coating | C-6 |
| ASTM A 121 |  |  |
| CLASS 1 | 4 pt. 12 ½ ga. Barb Wire .28 oz/ft.² Zinc Coating |  |
| CLASS 3 | 4 pt. 12 ½ ga. Barb Wire .80 oz/ft.² Zinc Coating | C-5 |
| ASTM A 585 |  |  |
| TYPE I | 4 pt. 12 ½ ga. Barb Wire .30 oz/ft.² Aluminum Coating | C-5 |
| TYPE II | 4 pt. 12 ½ ga. High Security Barb Wire .30 oz/ft.² Aluminum Coating |  |

| Pg.9 |
| --- |
| DATA – SPECIFICATIONS |
| FEDERAL SPECIFICATION |
| DESIGNATION | PRODUCT REQUIRED | PAGE NO. |
| RR-F-191/1D |  |  |
| TYPE I | Chain Link Fabric 1.2 oz/ft.² Zinc Coating | M-2, 4, 5 |
| TYPE II | Aluminized Chain Link Fabric | M-6 |
| TYPE III | Aluminum Alloy Chain Link Fabric |  |
| TYPE IV | Master Bond™ Chain Link Fabric | M-11 |
| RR-F-191/3D |  |  |
| CLASS 1 |  |  |
| GRADE A | Domestic Full Weight Pipe | J-20, 21 |
| GRADE B | DQ40 Pipe | J-15, 16 |
| AMERICAN ASSOCIATION OF STATE HIGHWAY AND TRANSPORTATION OFFICALS (AASHTO) |
| DESIGNATION | PRODUCT REQUIRED | PAGE NO. |
| M 181 FABRIC |  |  |
| TYPE I |  |  |
| CLASS C | Chain Link Fabric 1.2 oz/ft.² Zinc Coating | M-2,4,5 |
| CLASS D | Chain Link Fabric 2.0 oz/ft.² Zinc Coating | M-4 |
| TYPE II | Aluminized Chain Link Fabric | M-6 |
| TYPE IV |  |  |
| CLASS A | Master Bond™ Chain Link Fabric | M-11 |
| CLASS B | Fusion Bonded Chain Link Fabric | S-33 |
| M 181 POST |  |  |
| GRADE 1 | Domestic Full Weight Pipe | J-20,21 |
| GRADE 2 | DQ40 Pipe | J-15,16 |